1405/1410/1420 SERIES

INSTALLATION GUIDE

- INTRODUCTION

  - BASE COMPONENT

Figure1-1 Base Component Diagram

2. MECHANICAL INTEGRATION

The following information is intended as a guide for engineering purposes. It features the layout and mounting features, window dimensions and positioning.

2.1 MOUNTING OPTION

Figure 2-1 Outer Dimension Diagram

Figure 2-1 shows the outline drawing of the scan module, including the outgoing scan line and the electrical interface connector location. The scan module may be mounted in any orientation in your product using the three mounting holes shown in Figure 2-2, and a P-TYPE 2.6mm screw is recommended when mounting.

## Figure 2-2 Mounting Diagram

2WINDOW DESIGN

### A window in the housing is required to protect the module. The 1400 series module emits a LED red beam in a form of a scan line, the beam travels through the device’s window, reflects off the barcode symbol, returns through the window and is collected onto a CCD sensor. As in any optical system, any type of window will cause a reduction in scanning performance since some of the light is lost due to surface reflection. Beyond these reflection losses the light beam should not be materially degraded as it passes through the window.

### The design and placement of the window in the target device is critical for optimum performance.

### The following issues must be considered:

### The window must not block outgoing light

### The window must not block light reflected from the barcode. Figure 2-3 shows the minimum size and position of the window along the horizontal and vertical axis

### Out going light which is reflected from the window should not reach the front face of the scan module, either directly or through internal reflection within the host system. Such reflections generally have much greater optical amplitude than the reflection from the barcode symbol, and so can significantly reduce depth-of-field

## FIGURE 2-3 CLEAR APERTURE REQUIREMENT

You should determine the window tilt based on your application. The tilt angle of the window (that is, position relative to the optical axis or center- line) is important because a portion of the emitted light will always be specularly reflected from each of the two window surfaces. This specularly reflected light must not reach the CCD either directly or via multiple reflections from other parts of the module or the housing.

FIGURE 2-4 WINDOW PLACEMENT EXAMPLE

#### 3.CHARACTERISTICS

  - ELECTRICAL

3.1.1  Working voltage : 
1405 : 5V (10%
1410 : 3.3V (10%
1420 : 5V (10%

3.1.2  Typical operation current 
1405 :  <65mA
1410 :  <70mA
1420 :  <75mA

3.1.3  Standby current
1405 :  <15mA
1410 :  < 5mA
1420 :  <8mA

  - ENVIROMENTAL

    - Operating temperature(℃) : 0℃~50℃

    - Storage temperature(℃) : -20℃~60℃

    - Operating humidity : 10~90% non-condensing

    - Storage humidity : 0~95% non-condensing

  - PHYSICAL

    - Dimensions : 47 X 44 X 13 mm

    - Weight : 20g

  - OPTICAL

    - Light source : 630 nm Red LED

    - Resolution : up to 0.125 mm (5mil)

    - PCS : up to 0.45

    - Scan Rate : 100 scans/sec

    - Ambient light rejection : 2000 lux fluorescent, 1000 lux sun light

    - CCD Sensor:
1405 : 2048 pixels
1410 : 3648 pixels
1420 : 3648 pixels

  - INTERFACE

    - CMOS Level RS232, 1.25mm pitch 8pins connector

The 8 pin Male Header which mounted on the PCB

Is compatible with Molex 53047-0810 , the Female

Housing and Terminal(Molex 51021-0800 and 50058)

is recommended for a good connection .

    - Pin-assignment

| Pin # | Signal | Description |
| --- | --- | --- |
| 1 | TXD | 1410/1420 : CMOS RS232 1405 : Standard RS232 Transmit data pin, from module to Host (PC). |
| 2 | RXD | 1410/1420 : CMOS RS232 1405 : Standard RS232 Receive data pin, from Host (PC) to module |
| 3 | RTS | 1410/1420 : CMOS RS232 1405 : Standard RS232 RTS pin, from module to Host (PC) |
| 4 | CTS | 1410/1420 : CMOS RS232 1405 : Standard RS232 CTS pin , from Host (PC) to module |
| 5 | -Trigger | Switch input pin, active on falling edge |
| 6 | Indicator* | Indicator output pin, active Hi. |
| 7 | VCC | Power supply pin |
| 8 | GND | Ground |

* The LED indicator output can also be used to drive speaker.

    - DC Characteristics

| Parameter | Symbol | Min | Typ. | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| Power Supply Voltage | 1405/1420 | VCC1 | 4.5 | 5 | 5.5 | V |
|  | 1410 | VCC2 | 3 | 3.3 | 3.6 | V |
| Input Low Voltage | 1405 | VIL1 | 0.4 | 0.8 | - | V |
|  | 1410 | VIL2 | - | - | 0.3 VCC2 | V |
|  | 1420 | VIL3 | - | - | 0.3 VCC1 | V |
| Input Height Voltage | 1405 | VIH1 | - | 1.1 | 2.4 | V |
|  | 1410 | VIH2 | 0.7 VCC2 | - | - | V |
|  | 1420 | VIH3 | 0.7 VCC1 | - | - | V |
| Output Low Voltage | 1405 | VOL1 | -5 | -9 | - | V |
|  | 1410 | VOL2 | - | - | 0.45 | V |
|  | 1420 | VOL3 | - | 0 | 0.1 | V |
| Output Height Voltage | 1405 | VOH1 | +5 | +9 | - | V |
|  | 1410 | VOH2 | 2.4 | - | - | V |
|  | 1420 | VOH3 | 4.4 | 4.5 | - | V |

  - 1410/1420 DEMONSTRATION BOARD

    - Schematic

    - Pin-assignment of Connector (JP3)

| Pin# | Signal | Description |
| --- | --- | --- |
| 1 | RXD | Standard RS232 Receive data input pin. |
| 2 | CTS | Standard RS232 CTS input pin. |
| 3 | TXD | CMOS RS232 Transmit data output pin. |
| 4 | GND | Ground |
| 5 | NC |  |
| 6 | NC |  |
| 7 | NC |  |
| 8 | NC |  |
| 9 | NC |  |
| 10 | RTS | Standard RS232 RTS output pin. |

You can use our Cipher-1100 single RS232 cable, part No. is WSI6000100041, as the interface cable.

  - 1405 DEMONSTRATION BOARD

Use Standard RS232 DB9 Cable to Connect to PC

# Text boxes

Pin 1